## Slide 1: Slice Timing: Multiband & NIFTI .nii
AFNI can store EPI slice time offsets in the dataset header (*.HEAD)
Problem: Multiband (multi-slice) image acquisition has complicated slice timing/order
  Not just interleaved: 0 4 1 5 2 6 3 7
  Might be instead: 0 2 3 1 0 2 3 1 (multiband 2)
  Can be hard to read from DICOM files
Problem: The standard NIFTI .nii format cannot store complicated slice timings
  So programs like dcm2niix_afni cannot store this information even if the program can find it in the DICOM files

## Slide 2: AFNI and Slice Timing
I am assuming you have (or can find) the slice timing for your EPI datasets
  If you are downloading data from some other place, you might not be able to get that timing
  In that situation, you will just have to skip slice timing correction (tshift block in afni_proc.py)
It is possible to make afni_proc.py use slice timing that is not stored in the dataset header, but it is complicated right now
I plan to make a software change to AFNI to make it easier to store the slice timing in the NIFTI file, so 3dTshift can do good work - DONE