## Slide 1: Resting State Analysis
Pre-processing
Caveats & Kvetches
Tools

## Slide 2: Self-Referencing
Basic issue: No external information to “tie down” the analysis
  No task timing, no behavior measurements
Can only reference data to itself
Which means that statistical inference is tricky
Artifacts can reduce and/or increase inter-regional correlations of RS data

## Slide 3: Issues to Suffer With
Spikes in the data
Motion artifacts, even after image registration
Physiological signals
Long-term drifts = low frequency noise
Rapid signal changes = high frequency noise
  BOLD effect is slow, so signal changes faster than time scale of (say) 10 seconds aren’t (mostly) BOLD

## Slide 4: Solutions via Pre-Processing
Despiking the data
Slice timing correction
Motion correction
Spatial normalization, alignment of EPI to anatomy, segmentation of anatomy
Extraction of tissue-based regressors of no interest [e.g., ANATICOR (HJ Jo et alii)]
  Spatial blurring, if any, comes AFTER this step
Motion censoring + Nuisance regression [via RetroTS] + Bandpass filtering [all in one step]

## Slide 5: Things We Really Don’t Like
Global Signal Regression (GSR)
  Its effects on inter-regional correlations are unquantifiable, spatially variable, and can significantly differ between subject groups
  There is a strong interaction between GSR and subject head motion that is also confusing
Poor software implementations of the pre-processing steps
  and poorly written Methods sections of papers
Spatial blurring before tissue-based regressor extraction!

## Slide 6: RS-FMRI: Still Condensing from the Primordial Quark-Gluon Plasma
Data acquisition and processing for RS-FMRI is still unsettled
  MUCH more so than for task-based FMRI
How to deal with removal of various artifacts is still a subject for R&D
How to interpret the results is also up in the air
Convergence of results from different strains of evidence, and/or from different types of analyses is a good thing

## Slide 7: Tools in AFNI - 1
afni_proc.py will do the pre-processing steps as we currently recommend
  Results are ready-to-analyze individual subject time series datasets, hopefully cleaned up, and in standard (atlas/template) space
3dTcorrMap = compute average correlation of every voxel with every other voxel in the brain
  AKA “overall connectedness” of each voxel
3dTcorr1D = compute correlation of every voxel time series in a dataset with external time series in a 1D text file

## Slide 8: Tools in AFNI - 2
3dAutoTcorrelate = compute and save correlation of every voxel time series with every other voxel time series
  Output file can be HUMUNGOLIOUS
AFNI InstaCorr = interactive tool for testing one dataset with seed-based correlation
3dGroupInCorr = interactive tool for testing 1 or 2 groups of datasets with seed-based correlation

## Slide 9: Paper from NIMH
Illustrates how to process and think about RS-FMRI data
Fractionation of social brain circuits in autism spectrum disorders
SJ Gotts, WK Simmons, LA Milbury, GL Wallace, RW Cox, and A Martin
Brain 135:2711-2725 (2012)
doi: 10.1093/brain/aws160