## Slide 1: Resting State FMRI: Analysis Methods and Analysis Problems
SSCC / NIMH & NINDS / NIH / DHHS / USA / EARTH

## Slide 2: Resting state
  BOLD signal fluctuations during undirected brain activity

## Slide 3: Resting state
  BOLD signal fluctuations during undirected brain activity
  There is no model for signal, such as expected response in task FMRI

## Slide 4: Resting state
  BOLD signal fluctuations during undirected brain activity
  There is no model for signal, such as expected response in task FMRI
  Resort to describing relationships between brain regions
  Correlation matrices, graph theory, functional/effective/??? “connectivity”
    Factoring data into space×time components in statistically interesting ways (PCA, ICA)

## Slide 5: Resting state
  Resort to describing relationships between brain regions
Correlation Seed

## Slide 6: Resting state
  Interpret correlation strength as proxy (or stand-in) for brain function coupling between regions
Correlation Seed

## Slide 7: The magic of resting state
(Biswal 95)

## Slide 8: Resting state PROBLEM
  Neuronally driven BOLD fluctuations of interest
  AND
  Fluctuations from respiration, heart beat, motion
  Are all spatially correlated 

## Slide 9: The origin of our troubles
We have no model for signal
  Nothing like the expected response (regressors) of task FMRI
We have no good models for noise
  We have some, but they’re far from perfect
    Effect size (as correlation) is a spatially varying function of noise (fluctuations of no interest)
  Noise can bias correlations up, or down depending on the noise’s spatial covariance
  In task FMRI by contrast, noise affects variance of effect size estimate
Z.S.S 16/06/13

## Slide 10: The origin of our troubles
Difficult to attach meaning to effect size in RS-FMRI
  Effect in RS-FMRI is like an SNR measure, affected by changes in both signal (numerator) and noise (denominator)
  For example, if you have 2 groups
  more motion  more noise  more correlation (bias)  group differences
Weak but consistent bias  significant difference
Some sources have brain-wide (global) effects on correlation distribution (e.g. ET-CO2 , motion, etc.)

## Slide 11: Sources of bias and error
  Head motion (Van Dijk, 2012) (Power, 2012)
Physiological “Noise”
  Respiratory or cardiac cycles (Glover, 2002)
  Non-stationarity of breathing and cardiac rhythms (Birn, 2006) (Shmueli, 2007) (Chang, 2009)
Hardware instability (Jo, 2010)
Anatomical bias
Pre-processing

## Slide 12: AFNI’s recommended RS-FMRI pre-processing steps HJ Jo et al, 2010 and 2013 Carried out using afni_proc.py

## Slide 13: Step 1 = Despiking (before)

## Slide 14: Step 1 = Despiking (after)

## Slide 15: Step 2 = Slice Timing Correction
2D Slices acquired at different times within one 3D “volume” TR
Even the same physiological BOLD effect in 2 different slices will show up differently due to being measured at different times
And so will be less correlated than they “should be”
Solution: interpolate in time to some common reference point before calculating correlations
    Not perfect, because we are also interpolating noise

## Slide 16: Step 3 = Motion Correction Step 4 = Alignment with Anatomy Step 5 = Spatial Normalization
Step 3: Even more important for RS-FMRI, since the BOLD effect is smaller and more spatially diffused than in task-FMRI, so correcting for subject head motion is crucial
Step 4: Needed for step 5, and for assigning RS-FMRI results to brain regions
Step 5: Needed for group studies

## Slide 17: Step 6 = Extract Tissue Based Regressors
The purpose of tissue based regressors is to extract fluctuations that are not BOLD signal
So we can regress them out of the data at step 8
Common choices include:
    Average white matter (WM) signal time series
    Several principal components of all WM time series (CompCor method)
    Average global brain signal time series (GS) 
    Average signal from CSF in ventricles
Less common (only in AFNI): ANATicor …

## Slide 18: ANATicor – Tissue Based per voxel
Eroded WM
mask (WMe)
Average over
WMe voxels
inside 25mm
radius

## Slide 19: Step 7 = Spatial Blurring
Important for RS-FMRI since the BOLD signal fluctuations are small
So averaging locally will tend to cancel noise and add up coherent signals
Important: blur after tissue based signal extraction
Otherwise, will get unintended signals in WM and CSF that were blurred in from nearby GM (gray matter)

## Slide 20: Effects of Blurring on Correlation
Is this a pure vascular/cardiac effect being progressively smeared? Or real neural correlations seen via BOLD? Or some of both?
0mm
1mm
2mm
3mm
4mm
5mm
6mm
7mm

## Slide 21: Step 8 = Nuisance Regression - 1
In task-FMRI, regression is to find the signal amplitudes of the task model components while at the same time removing the nuisance model components
    Nuisances: motion parameters, motion parameter time derivatives, WM signals, measured respiration signal, etc
In RS-FMRI, there are no task model components to estimate
All we want is to remove the nuisance components and compute the residuals – these residuals are the output, ready for correlations

## Slide 22: Step 8 = Nuisance Regression - 2
Another operation usually (but not always) used in RS-FMRI is called bandpassing
It involves removing all frequency components from the data except those in a specific band
Frequency: units are Hertz (Hz)
    1 Hz = 1 cycle per second
    0.01 Hz = 0.01 cycle per second = 1 cycle in 100 seconds
    100 Hz = 100 cycles per second = 1 cycle in 0.01 seconds
  In RS-FMRI, it is common to bandpass out all frequencies higher than 0.10 Hz and smaller than 0.01 Hz
    Keep only 10-100 second cycles; faster or slower = OUT
  The idea is that these do not contain BOLD, just noise, so should be removed before correlation

## Slide 23: Step 8 = Nuisance Regression - 3
It is also common to censor out “bad” time points, so they aren’t used in the correlation
    “Bad” = too much motion, or that volume has too many “outlier” data points
It is important to censor bad time points before the nuisance regression
    Otherwise, they will affect the regression results and contaminate residuals even at the un-censored times
  In AFNI, nuisance regression, bandpassing, and censoring for RS-FMRI are all done in the same program: 3dTproject
    Which allows for voxel-specific regressors (ANATicor)

## Slide 24: Step 8 = Nuisance Regression - 4
Some people did these 2 steps in sequence:
    Bandpass the data
    Regress other nuisance components from the bandpassed data
  Doing these operations in 2 steps (instead of one) is not just bad, it is WRONG
  Since the nuisance regressors will contain some of the unwanted frequency components, these unwanted components will “leak” back into the data at the second regression
    If the nuisance regressors were bandpassed themselves, then the problem would not happen
  The same thing applies to bandpassing and censoring – they should be done together
  These reasons are why 3dTproject was written

## Slide 25: AFNI’s recommended RS-FMRI pre-processing steps HJ Jo et al, 2010 and 2013 Carried out using afni_proc.py

## Slide 26: Preprocess via afni_proc.py
## Adapted from Example 9b in afni_proc.py –help
afni_proc.py -subj_id s620 \
-dsets s620_rest_r1+orig.HEAD \
-blocks despike tshift align tlrc volreg \
blur mask regress \
-tcat_remove_first_trs 2 \
-volreg_align_e2a \
-blur_size 6 \
-regress_anaticor_fast \
-regress_censor_motion 0.2 \
-regress_censor_outliers 0.1 \
-regress_bandpass 0.01 0.1 \
-regress_apply_mot_types demean deriv \
-regress_run_clustsim no -regress_est_blur_errts

## Slide 27: Adjusting brain-wide nuisances
Model noise effect on time series and project
  Motion estimates
  Retroicor/RVT/etc requires simultaneous recordings of cardiac and respiratory cycles
  (Glover 2002; Birn 2006; Shmueli 2007; Chang 2009)
  Nuisance signals estimates from dataset
  Tissue-based nuisance regressors
  (Beckmann 2004; Fox 2009; Behzadi 2007; Beall 2007, 2010;
  Jo 2010, 2013; Kundu 2012; Bright 2013; Boubela 2013)
Group level adjustments
  Covariates for motion, brainwide levels of correlation
    (Van Dijk 2012; Satterthwaite 2012; Saad 2013; Yan 2013)

## Slide 28: AFNI Progams for Correlating - 1
3dTcorr1D = correlate all time series in a dataset with time series in a text 1D file
3dTcorrMap = correlate each voxel time series in the input with every other voxel, combine these correlations in some way (linear, nonlinear), save that combined correlation as a measure of how “connected” each voxel is with the rest of the brain
3dAutoTcorrelate = correlate each voxel time series with every other voxel, and save all of these correlations
    Output dataset will be HUGE unless you are careful and use a gray matter only mask (e.g., program 3dSeg)

## Slide 29: AFNI Progams for Correlating - 2
AFNI GUI InstaCorr – single subject seed based correlation by pointing and clicking
    Subject of another talk
3dGroupInCorr – group analysis of seed based correlations, also by pointing and clicking
    Also in the InstaCorr presentation
  AFNI does not contain a program for doing ICA for network parcellation or identification from RS-FMRI data
    GIFT software from Vince Calhoun lab, for example
    http://mialab.mrn.org/software/gift/

## Slide 30: Tissue-based nuisance regressors
Avoid Projecting Fluctuations of Interest
OK to sample nuisance signals from regions whose fluctuations are not correlated with the fluctuations of interest in the regions of interest
Should not project time series containing aggregates of fluctuations of interest, even if they contain contribution from noise
    Sagittal sinus voxels might allow sampling of aliased heart rate, HOWEVER they also exhibit BOLD fluctuations of interest from the regions being modeled (Jo, 2010)

## Slide 31: And why not?
Because you will end up differentially biasing the correlation matrices of your groups, and considerably distorting group differences
Best explained with GSReg (using the Global Signal as a nuisance Regressor) because math is straight forward.
  What follows applies whether or not noise exists or differs between groups

## Slide 32: Why not GSReg ?
Original (R)
After GSReg (S)
S - R
Bias will vary by region pair
AND will be
Entirely dependent on true covariance matrix P
(therefore your grouping variable)

## Slide 33: Why not GSReg ?
Original (R)
After GSReg (S)
S - R
For any FMRI time series (not just simulations)
S-R is constant for group with same cov. matrix P
(Q is also a sole function of P) (Saad, 2013)

## Slide 34: Are biased estimates useful?
Region pair dependent biasing is OK if:
  Not interpreting correlations between regions as those between the sampled BOLD signals and by extension neuronal signals
      Not just about interpretability of negative correlations (Murphy, 2008; Weissenbacher, 2009; Cole, 2010)
      Two strongly correlated regions after GSReg DOES NOT imply regions were strongly correlated before GSReg
  Using correlations after GSReg as some feature space for parcellation, classification, etc

## Slide 35: Are biased estimates useful?
Region pair dependent biasing is OK if:
  Not interpreting correlations between regions as those between the sampled BOLD signals and by extension neuronal signals
      Not just about interpretability of negative correlations (Murphy, 2008; Weissenbacher, 2009; Cole, 2010)
      Two strongly correlated regions after GSReg DOES NOT imply regions were strongly correlated before GSReg
  Using correlations after GSReg as some feature space for parcellation, classification, etc
Region pair dependent biasing is problematic if:
Comparing two groups with possibly different signal covariance structures
S-R is constant for group with same cov. matrix P
S-R will differ between groups with different P

## Slide 36: An illustrative model
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Group ψ
Observed signal from region 4:
y4 = V w4 + e = 0.36 v0 + 0.66 v3 + 0.36 v4 + 0.54 v5 + e
w0
w1
w2
w3
w4
w5
w4 connection weights for region 4
0.3
1.0
Connection Weight
In simulations 9 regions + background were used

## Slide 37: Comparing Groups
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Group ψ
Group ψL
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Increased connection between regions 1 and 2 only

## Slide 38: Comparing Groups
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Group ψ
Group ψL
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Difference confined
to two regions

## Slide 39: Comparing Groups
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Group ψ
Group ψL
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Difference confined
to two regions
Ends up all
over the place

## Slide 40: Distortion of long/short range correlations
Contrast of correlations between groups A and B
‘long-range’ correlations in Group B only
(Saad, 2012, Gotts 2013)

## Slide 41: Comparing Groups with GSReg
One seeks and hopes for differences in covariance/correlation structures between groups.
  Using GSReg means each group will be biased DIFFERENTLY for different region pairs.
    Even in the absence of noise difference, you can find group correlation differences in places where none existed before.
      OK if you’re teaching a classifier to differentiate between the two groups.
      NOT OK if interpreting correlation differences to evoke correlation differences of neuronally induced BOLD signal between these regions.
  With noise previous problems remain
    However bias now depends on the covariance structures of noise and signals of interest though we can’t tell them apart.
    Interaction between GSReg projection effects and grouping variable remains

## Slide 42: SAME holds with empirical data
+ GCOR
Z=-15
X=-27
X=+30
X=-43
X=+51
Z=+10
ANATICOR
Z=-15
X=-27
X=+30
X=-43
X=+51
Z=+10
(Gotts, 2013)
+ GS Regression
Z=-15
L
X=-27
X=+30
X=-43
X=+51
Z=+10
TD>ASD
ASD>TD
t-val (N=60)
2.0
≥ 4.0
-2.0
≤ -4.0
(Jo, 2010)

## Slide 43: SAME holds with empirical data
(Gotts, 2013)

## Slide 44: It is not just GSR
Nuisance regressors correlated with fluctuations of interest in regions of interest (not the noise) will cause the same problems.
Non-gray matter averages may be comparable to GSReg (partial voluming with grey matter)
  Averaging over small regions of eroded non-gray matter tissue are advantageous (Jo, 2010, 2013)
Decomposition methods that cannot separate BOLD (fluctuations of interest) from noise also problematic.

## Slide 45: The Siren’s Song
What of results being more stable after GSReg?
  There is a denoising component to the approach and bias is consistent for consistent covariance structure
    However, interpretation of correlations is now difficult (Cole, 2010)
    Interaction effect with grouping variable completely ignored
    Differences can get spread in unknown ways
    Tests of processing methods should always consider group comparisons
What of GSReg for motion compensation?
Some denoising effect  reducing residual variance and motion-based group differences
  However, caveats from above remain
  AND are we actually compensating for motion?

## Slide 46: Grouping Based on Motion
FCON 1000: Cambridge_Buckner
Mean Motion
Small Movers
Mean Motion
Big Movers

## Slide 47: Grouping Based on Motion
FCON 1000: Cambridge_Buckner
4 clusters
Largest 4 Clusters

## Slide 48: Grouping Based on Motion
FCON 1000: Cambridge_Buckner
Largest 4 Clusters
4 clusters
3 clusters

## Slide 49: Grouping Based on Motion
FCON 1000: Cambridge_Buckner
Largest 4 Clusters
4 clusters
Group Difference, p<0.01, α=0.05
Small > Big
Small < Big
[
[
FCON 1000: Beijing_Zang
(none)
1 cluster
0 clusters
29 μm/TR
25 μm/TR
(Saad, 2013)
More Motion
More Motion Difference
Much less group difference!

## Slide 50: Grouping Based on Motion
Note weak correlation between motion and GCOR (R2=11% Cambridge, 4.3% Beijing)
Mean Motion
Big Movers
Mean Motion
Small Movers
FCON 1000: Cambridge_Buckner
FCON 1000: Beijing_Zang
The average correlation of every voxel with every other voxel in the brain

## Slide 51: Can GSReg help with motion?
Censoring (scrubbing) high motion samples changes inter-regional correlations in distance dependent manner.
 suggests effect of motion on correlations depends on distance between regions (Power et al. 2012)
 importance of censoring high motion
Data generously made public by Power & coauthors 2012

## Slide 52: Can GSReg help with motion?
Censoring (scrubbing) samples of high motion changes inter-regional correlations in a distance manner.
 suggests effect of motion on correlations depends on distance between regions (Power et al. 2012)
 importance of censoring high motion
Less dependence without GSReg

## Slide 53: Can GSReg help with motion?
Censoring (scrubbing) samples of high motion changes inter-regional correlations in a distance manner.
 suggests effect of motion on correlations depends on distance between regions (Power et al. 2012)
 importance of censoring high motion
Least dependence

## Slide 54: Can GSReg help with motion?
GSReg  Correlation more sensitive to motion
 Correlation more sensitive to censoring
Improved denoising largely eliminates distance dependent bias
(Jo, 2013)

## Slide 55: Sampling nuisance TS regressors
Sample noise without aggregating over regions with fluctuations of interest
  Erode white matter masks to avoid partial voluming
  Avoiding regions with fluctuations of interest
  Local eroded white matter masks improve denoising without increasing DOFs
Use decomposition methods that can separate BOLD from non BOLD fluctuations of interest
    or attempt to identify noise components
Use noise models RICOR/RVT/etc.
(Jo, 2010, 2013)
(Kundu, 2012, Bright, 2013)
(Beckmann 2004, Beall 2010, Boubela, 2013)
(Glover 2000; Shmueli 2007; Birn 2008; Chang 2009)
(Anderson 2011)

## Slide 56: Brain-wide correlation adjustments?
If subject to subject variations in brain-wide correlations exist, why not correct for them?
Consider GCOR, the average over the entire correlation matrix of every voxel with every other voxel
  Measure would be costly to compute if one had to estimate the entire correlation matrix first.
  However estimating GCOR is trivial:
gu is the average of all (M) unit variance time series of length N in matrix U
(Saad, 2013)

## Slide 57: GCOR as group level covariate
Using models described earlier, we consider group level correlation (differences) from three models:
  No adjustment:
  GSReg at level I:
  GCOR as covariate:

## Slide 58: Less bias than with GSReg for 1 sample tests
1
2
3
4
5
6
7
8
9
region

## Slide 59: Comparing Groups
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
Group ψ
Group ψL
4
5
3
1
2
background
0.36
0.66
0.63
0.54
background
4
5
3
1
2
background
0.66
0.63
0.54
background
Group ψB
Group ψBL
4
5
3
1
2
background
0.66
0.63
0.54
background
More
Local
More
Cowbell
More
Backg.

## Slide 60: Group Contrast, Only Local Change

## Slide 61: Group Contrast, Local & Backg. Change

## Slide 62: GCOR and Motion Grouping
FCON 1000: Cambridge_Buckner
FCON 1000: Beijing_Zang
Δ=25 μm/TR
Δ=29 μm/TR
Mean GCOR
Small Movers
Mean GCOR
Big Movers
Mean Motion
Big Movers
Mean Motion
Small Movers

## Slide 63: GCOR and Motion Grouping
FCON 1000: Cambridge_Buckner

## Slide 64: GCOR as Group Level Covariate
Correlations less biased with GCOR, than GSReg.
when GCOR has low correlation with grouping variable
Level-II tests conservative
Less likely to detect difference as grouping variable and covariate correlation increases
Adjustment outside of level II test is NOT recommended
There is always potential for interaction effect with group
GCOR (and other params. (Yan 2013)) depend on noise AND/OR inter-regional correlations of interest
contrast results very likely depend on covariate centering
      Centering at overall mean makes sense if GCOR is driven by noise.
      What if it is also driven by correlations of interest?
 contrast sign might even get reversed

## Slide 65: Conclusions
Stay away from using regions with Fluctuations of Interest to calculate regressors of No Interest
GSReg and its variants are bad for inter-group comparisons
One MUST consider interactions of method with grouping variable
  Generative models clarify matters since there is no base truth
GCOR is very simple to compute and is useful to assess global correlation levels
Use of GCOR and comparable measures is better than GSReg
  However, their interaction with grouping variable can confound interpretation
Use should be as last resort
    Use them as covariates and consider interaction terms
    Separate covariate modeling prior to level-II not recommended
    Risks of false negatives
    Centering issues

## Slide 66: Conclusions
The best approach remains with careful denoising
    motion parameter estimates
    physiological measurements (chest belt = plethysmograph, pulse oximeter, end tidal CO2 = ET-CO2)
    local estimates of nuisance signals from eroded white matter
      ANATicor, CompCor
    denoising decompositions in as far as they can dissociate nuisance estimates from signal fluctuations of interest
Look at your data

## Slide 67: Acknowledgments
Robert W. Cox
Hang Joon Jo
Rick Reynolds
Alex Martin
Steve Gotts
Kelly Barnes
Robert Cox
Gang Chen
Steve Gotts
Hang Joon Jo
Alex Martin
Rick Reynolds
Kelly Barnes
Catie Chang
Carlton Chu
Jonathan Power
and coauthors
for releasing data