## Slide 1: Equitable Thresholding And Clustering (ETAC)
Robert W Cox
SSCC / NIMH / NIH / DHHS / USA / EARTH
https://afni.nimh.nih.gov
2017
Ahu Akivi

## Slide 2: Voxel-Wise Group Analysis
Do first level time series analysis on each subject’s data separately
  Transformed to common template (e.g., MNI)
    Best with nonlinear transformation (3dQwarp)
      Can restrict analysis to dilated gray matter mask
Second level group analysis on voxel 𝛃 values = % signal change (not ROIs)
  Can be as simple as t-tests (3dttest++)
  Or a complicated model such as Linear Mixed Effects (3dLME), etc.
Notes: Questions about 3dQwarp? Ask me later.

## Slide 3: Aside: Whole Brain Mask

## Slide 4: Dilated GM Mask (≈60% of WB)
Recommend use of script @SSwarper

## Slide 5: Group Spatial Inference - 1
Goal: control global False Positive Rate (FPR) – to 5% level (e.g.)
  FPR = FWE = Family-Wise Error
    = rate of errors across the family of voxel tests
    “error” = when anything is found in noise-only data vs the null hypothesis (i.e., no “activity”)
Different approach: to control the False Discovery Rate (FDR, voxel-wise)
  = fraction of ”discoveries” that are “errors”
  Not what I’m going to talk about here
    Difficult to allow for inter-voxel correlation in noise
Notes: Super conservative because so many voxels = so many tests = even a small per-voxel FPR gives a large global FPR

## Slide 6: Group Spatial Inference - 2
Voxel-wise thresholding on group t-statistic is usually super conservative (to get global FPR≈5%)
  Can estimate false non-discovery rate (FNDR of voxels) using adaptation of voxel-wise FDR algorithm
    Not highly accurate, nor widely used in FMRI
    An algorithm for this estimate is hidden in AFNI
  Typically 60-90% (or more)
    Depends on number of subjects (i.e., statistical power) – figure above is for ≈20 subjects
Notes: Super conservative because so many voxels = so many tests = even a small per-voxel FPR gives a large global FPR

## Slide 7: Group Spatial Inference - 3
A Solution: form clusters of neighboring voxels, each above a lower (less strict) voxel-wise t-statistic (or z-statistic)
  With a larger voxel-wise p-value (=smaller t )
Then: threshold on cluster-size as well
  Or some other cluster-FOM (Figure of Merit)
    e.g., Sum over cluster of voxel-wise z2
    Reject small/weak isolated clusters
  Given voxel-wise p, adjust cluster-FOM threshold to get desired global FPR ➾➾…
Notes: Solution started with PET, adopted early on in FMRI (by 1995 or so)

## Slide 8: Group Spatial Inference - 4
Double threshold method (voxel then cluster) can be weak (low power to detect)
A Solution: use spatial blurring ≈ average nearby voxel 𝛃 (“Coef ”) values together, in each subject, before group statistics
  To reduce noise and reinforce commonality
  To reduce effective number of independent statistical tests (but lose spatial resolution)
  To select the minimum spatial scale of what we are hunting for

## Slide 9: 1D Double Thresholding (real data)
6 mm blur

## Slide 10: 1D Double Thresholding (real data)
6 mm blur

## Slide 11: 1D Double Thresholding (real data)
6 mm blur

## Slide 12: 1D Double Thresholding (real data)
6 mm blur

## Slide 13: (Semi-) Arbitrary Choices
I’ve mentioned two parameters that must be chosen by the researcher:
  Voxel-wise p-value for first-level thresholding
    Typical values range from 0.001 to 0.01
  Amount of spatial blurring to add to data
    Typical values range from 4 to 10 mm
But there are no “best” values 
  ETAC can rescue you! (from these choices) 

## Slide 14: Old ClustSim - 1
Spatial correlation of “noise” in FMRI data means no exact formula for cluster-FOM threshold, for a given p threshold
So: Assume Gaussian-shape for spatial auto-correlation function (ACF) of noise
  Fit Gaussian width parameter (Forman 1995)
  Use approximate formula (SPM) or Monte-Carlo simulation (AFNI) to get cluster-size threshold
    SPM method possible due to Gaussian ACF
Notes: Why a Gaussian ACF? Partially from notion of multiple types of blurring end up as Gaussian. Also arose in analysis of PET data, which has little intrinsic spatial correlation

## Slide 15: Old ClustSim - 2
Generate random noise-only dataset with Gaussian ACF (with chosen FWHM)
Threshold at various per-voxel p-values
Find largest cluster in brain mask
Repeat steps 1-3 10,000+ times
For each per-voxel p-value, cluster-size threshold is largest cluster size which occurs only in 5% (e.g.) of cases
Notes: Simple in concept. Careful programming needed to make efficient.

## Slide 16: ClustSim: Table of Sizes Found
size count
1 1830
2 2106
3 1572
4 1204
5 792
6 595
7 405
8 302
9 177
10 127
11 82
12 45
13 44
14 32
15 12
16 13
17 11
18 9
19 6
20 5
21 2
22 3
23 0
24 3
25 0
26 1
27 0
28 0
29 1
Out of 10000 simulations
Smallest cluster size with < 500 false positives (5% FPR) above
Add up until total just less than 500
Notes: 396 to be exact

## Slide 17: ClustSim - 4
3dClustSim outputs tables like this:
# CLUSTER SIZE THRESHOLD(pthr,alpha)
# -NN 2 | alpha=Prob(Cluster > given size)
# pthr |.10000 .05000 .02000 .01000
# ------ | ------ ------ ------ ------
0.010000 50.3 57.2 66.3 73.6
0.005000 34.4 39.5 46.3 51.6
0.002000 22.1 25.7 30.4 34.1
0.001000 16.0 19.0 22.8 26.0
0.000500 12.0 14.5 17.4 20.1
0.000200 8.1 10.0 12.6 14.6
0.000100 6.1 7.7 9.9 11.6
  ➾
Notes: e.g., p=0.002 and desired FPR=5%  cluster-size threshold = 26 voxels

## Slide 18: ClustSim - 5
High t threshold ➾ small cluster threshold
Voxel configurations in
here will be accepted
5% FPR tradeoff curve
Cluster-size threshold
-log(p) or t- or z-statistic voxel-wise threshold
Notes: Grand Canyon hiking idea

## Slide 19: FPR: Testing Some Method
Eklund et al: use rsFMRI (FCON-1000) as null data
  Analyze each of 198 x 2 subject collections (Beijing and Cambridge) with fake task timings
    2 x Block design, 2 x Event-related design
    4 x spatial blur levels (4, 6, 8, 10 mm)
  Carry out 1- and 2-sample t-tests between subsets of these collections – 1000 random subsets (per case, per collection, per diverse variations)
  Count clusters surviving the given software, get FPR estimate
Scripts and tabular results available on GitHub
}
16 basic
cases

## Slide 20: Old ClustSim - We Got Trouble
Eklund et al, PNAS 113:7900-7905 (2016)
• FPR≫5%: notably for voxel-wise p=0.01
• A lot of doom-crying about this in 2016:
“Could Invalidate 15 Years of Brain Research ”
AFNI’s
3D t-testing program
AFNI’s
3D t-testing program

## Slide 21: All Their Results Summarized
Box plots across all cases: 1- and 2-sample, various sample sizes, various “stimuli”, various data sources
“Up to 70%” FPR (triply-used quote from Eklund et al) is not a decent summary of the situation.
Eklund et al’s method
Notes: Up to 30% would have been more reasonable IMHO

## Slide 22: Rest: A Good Null for Task?
Is rsFMRI data a good/valid null case for task-based analysis?
  Perhaps it has some task-like temporal structure being uncovered by accident?
  Is it more correlated in space than the noise (residuals) in task-based datasets?
    Not in the datasets I’ve looked at (cursorily)
My opinion:
  rsFMRI not perfect as a null, but as real data, it is reasonable to use it (vs simulations)

## Slide 23: 1 Fix + 3 Solutions in AFNI
0 ) Fix 3dClustSim bug found by Eklund
Extend ACF model in 3dClustSim to be more complicated than a Gaussian shape (the mixed model)
Eliminate ACF modeling by extending 3dClustSim to directly use residuals from 3dttest++ via randomization
Generalize cluster-thresholding model in several more directions: ETAC
Notes: The outline of my life from July 2016 to June 2017

## Slide 24: 0) Bugs and Flaws
AFNI’s cluster-size threshold calculating program (3dClustSim) had a bug
  A big deal in the PNAS paper (and popular press)
  Not actually that important (cf 5 slides ahead)
  Forman method for FWHM estimate = another flaw (FHWM = Full Width at Half Maximum)
    Using statistics of nearest-neighbor differences of noise to estimate FWHM of noise correlation
RWC: Feb 2017
FWHM
Notes: Forman method = estimate FWHM from moments of first-differences of noise (residuals)

## Slide 25: 0) Bugs and Flaws
However, there was/is a much bigger flaw
  Shared with FSL and SPM for unnumbered years
  Assumption of Gaussian shape for spatial autocorrelation function (ACF) of the noise
    ACF(r) describes how noise in one voxel is correlated with noise in another voxel (distance r away)
We are interested in clusters caused by true differences in signal
But we also have to study clusters caused by noise (signal fluctuations)
  Estimate probability of results being “bad luck”
RWC: Feb 2017
Notes: Forman method = estimate FWHM from moments of first-differences of noise (residuals)

## Slide 26: 1) NonGaussianity in ACF
ACF from single subject datasets has long tails – nonGaussian shape + 1st difference fail
Modify 3dClustSim to use mixed ACF model (Gaussian plus mono-exponential) with 3 parameters (a,b,c) instead of 1 (FWHM)
ACF(r)=exp[-)]]
1st-diff bad for FWHM estimate: too small;
Forman
method
unreliable
Notes: Where did this idea come from? A simple plot of log(ACF) vs r

## Slide 27: 1) Updated ClustSim
Program 3dFWHMx now estimates the mixed model (a,b,c) ACF parameters
  No longer shows Forman estimates
Program 3dClustSim takes ACF parameters and
  Simulates random noise-only 3D dataset with mixed model ACF
    A little slower than Gaussian ACF approach
  Otherwise, the same method as before:
    Builds tables of cluster sizes found
Notes: Note ACF is still assumed to be the same everywhere = “stationary”

## Slide 28: 1) ¿Do Long Tails Matter? Yes…
Compare cluster-size thresholds for 198 subjects
Computed via 3dClustSim using 2 different ACF models
In words: don’t use Gaussian ACF for FMRI (as is usually done)
  NB: Gaussian FWHM taken from mixed model ACF (not Forman)
x=y line
x=y line
Notes:   Has longer tails ➾ voxel noise is more correlated ➾ noise-only clusters more likely

## Slide 29: 0 & 1) AFNI Results Redux
Pre-bug fix
Post-bug fix
Mixed-model ACF
p=0.010
p=0.005
p=0.001
Notes: Column 1-2  ”bug” fix did relatively little
Column 2-3  ACF helps for some, but not enough to be close to 5% for larger p-values

## Slide 30: Resampling & Smoothness
Frontiers commentary (K Mueller et al, June 2017)
  Examined effect of resampling voxel size on smoothness estimates in SPM (47 datasets; 8 mm blur)
Smoothness goes down as resampled voxel size goes down ⇒ cluster-size threshold volumes go down ⇒ “more sensitive★”
2 mm
★ KJ Friston
Smoothed by 8 mm

## Slide 31: Resampling & Smoothness
Same calculation in AFNI (78 datasets from UCLA Phenomics study @OpenFMRI)
  Using mixed model ACF FWHM estimate
Little change in smoothness estimates with resampled voxel size (perhaps a slight drift upwards?)
2 mm
Gaussian FWHM estimate also stable w.r.t. resampling size

## Slide 32: Resampling & Smoothness
Same calculation in AFNI (78 datasets from UCLA Phenomics study @OpenFMRI)
  Using mixed model ACF FWHM estimate
Little change in smoothness estimates with resampled voxel size (perhaps a slight drift upwards?)
Note y-axis scale change
2 mm

## Slide 33: Resampling & Smoothness
Same calculation in AFNI (78 datasets from UCLA Phenomics study @OpenFMRI)
  Using mixed model ACF FWHM estimate
Cluster-volume thresholds () for resampled voxels sizes =
3, 2, & 1 mm

## Slide 34: 1) How to: ACF method
Run 3dFWHMx with ‘-acf’ option to get (a,b,c) for each subject, from residuals dataset errts*+tlrc.HEAD
  This calculation is done now in afni_proc.py
  Average each of the 3 ACF parameters across subjects (not automatic)
Use 3dClustSim with ‘-acf’ option (giving it the 3 averaged parameters) to get cluster size threshold tables for group analysis
  This method is OK, if per-voxel p 0.002

## Slide 35: ¿Why Is Model-Based FPR Still High?
Using ACF mixed model improved results
  So the wider ACF and longer tails are a part of the original problem – but not all of it
Too short tails in the group t-statistics, caused by outlier subjects in the data
  Also explained a part of it – but not very much
Spatial ACF is not stationary (same everywhere)
  Over-wide in some places
  Drives up FPR in those regions
FWHM
Notes: Could develop non-stationary ACF model for ClustSim – but that is not the approach I have followed to date

## Slide 37: 2) A Different Solution: Nonparametric Clustering in AFNI
t-test residuals are permuted/randomized (10000 times)
10000 re-t-tests computed from residuals fed to 3dClustSim
Notes: Global FPR control is as desired

## Slide 38: 2) How to: Nonparametric Clustering
Only for t-tests at this time
  Re-running many 3dLME cases (e.g.) is too slow
3dttest++ with the –Clustsim option
Gives excellent FPR control 
Has stringently large cluster-size thresholds 
  Seems to be needed to deal with the extra-wide spatial ACF in some regions (notably, midline)
  Cluster-size threshold is nonlinear in smoothness
  Leads to the idea of making the cluster-size threshold depend on spatial location ➾➾ …
RWC: Feb 2017
Notes: Large cluster size thresholds here inspired ETAC -- plus a hike over Brown’s Pass in Colorado

## Slide 39: 3) ETAC
Equitable Thresholding And Clustering
Uses multiple sub-methods at same time
  Equity = balancing FPRs of sub-methods
Voxel-wise thresholding at multiple p-values, then cluster-FOM thresholding
Multiple cases of spatial blurring
Different cluster-FOM thresholds in different brain regions (vs global thresh)
No model for ACF: uses randomization
  
Notes: Potential to find both small intense and large weak clusters
Remove some arbitrariness from group thresholding decisions

## Slide 40: Equity: A Toy Example
Is mean of a set different from 0?
  Compute t-statistic from the set
Method #1: accept if t > X
  Occurs by chance: probability = A(X )
Method #2: accept if t < −Y
  Occurs by chance: probability = A(Y )
  Accept either case (2-sided): A(X )+A(Y )
    Get 5% FPR with many combinations of X & Y
  Equity says: take X =Y ➾ normal 2-sided test
1-sided
tests
Notes: Balance FPR from #1 and #2 unless there is some extrinsic reason not to do this

## Slide 41: Equity: Multi-Thresholding
Voxel configurations in
here will be accepted
Voxel configurations in here will be accepted;
Individual thresholds fall along
the same t-vs-cluster-size
tradeoff curve = equity (balance)
Single per-voxel
p-value threshold
giving 5% global FPR
Four per-voxel p-
value thresholds, adjusted
to give 5% global FPR
= 5% FPR tradeoff curve
< 5% FPR tradeoff curve
-log(p) or t- or z-statistic voxel-wise threshold
Cluster-size threshold
Adjust to
make final
FPR 5%
This is what
ClustSim
computes
Notes: This is the Grand Canyon inspired figure

## Slide 42: Equity: Across Methods
Balancing can apply to any multi-choice method for selecting voxel clusters
  Each sub-method has a cluster-FOM threshold adjustable to get desired FPR
  Balance = choose each sub-method’s cluster-FOM threshold to have the same global FPR α0 < αGoal (e.g., 5%)
ETAC method (set union): accept a voxel if it survives at least one sub-method
  Adjust α0 up or down to get final FPR = αGoal
Notes: Generalization and abstraction of the previous figure

## Slide 43: Equity: Across Blur Cases
Blurring at (e.g.) 4, 6, 8, 10 mm
Potential to detect both small intense clusters and larger weak clusters
  Blur = 10 mm might “wash out” small cluster
  Blur = 4 mm might not reduce noise enough to find larger weak cluster
Combined with multi-thresholding (different p-values), reduces number of arbitrary choices to make in thresholding
Notes: Slightly different than multiple p-values in that different datasets need to be processed for each blur case  input datasets for t-tests that have been blurred differently for each case

## Slide 44: Equity: Across Space
Smoothness (ACF) of noise varies across the brain
  Using same cluster threshold everywhere will make FPR non-uniform
  Could try to differentially smooth to make ACF more uniform (not implemented in AFNI)
ETAC method: Use different cluster-FOM thresholds at different locations
  For each sub-method, produce a 3D map of the cluster-FOM threshold to use
Notes: This concept is the Brown’s Pass inspiration

## Slide 45: ETAC: Global FPR Control
10s blocks
30s blocks
regular events
random events
p = 0.01, 0.005, 0.003, 0.002, 0.001 blurs = 4, 6, 8, 10
1000 simulations each
Notes: Reasonably close to 5% level
1000 simulations (each) from rsFMRI datasets

## Slide 46: ETAC: Global FPR Control
p = 0.01, 0.005, 0.002, 0.001 blur = 4, 7, 10
1000 simulations each
2-sample
Notes: Reasonably close to 5% level
1000 simulations (each) from rsFMRI datasets

## Slide 47: ETAC: Global FPR Control
p = 0.01, 0.005, 0.002, 0.001 blur = 4, 7, 10
1000 simulations each
1-sample
Notes: Reasonably close to 5% level
1000 simulations (each) from rsFMRI datasets

## Slide 48: ETAC: Global FPR Control
p = 0.01, 0.005, 0.002, 0.001 blurs = 4, 7, 10
1000 simulations each
3 stimuli x (1-sided & 2-sided tests)
Various FPR αGoal from 2%‒9%
Notes: Reasonably close to 5% level
1000 simulations (each) from rsFMRI datasets

## Slide 49: Dataset Resampling
Eklund-Nichols resampling methodology:
  Given 198 datasets, choose 40 of them
  1-sample tests = all 40 in one sample t-test
  2-sample tests = 20 per sample
  Do this 1000 times
  But … the 1000 samples aren’t independent
In 1-sample tests, FPR results much wilder (bigger variance) than should be
  Verified by doing yet more simulations ➾ …

## Slide 50: 500 Noise-only Simulations
Each simulation runs 1000 3D t-test cases (40 datasets, 1 sample) and does cluster-detection (fixed cluster-size threshold, not ETAC – for speed)
Left column: all 40,000 inputs are independent in each simulation
Right column: inputs resampled from 198 datasets in each simulation

## Slide 51: 500 Noise-only Simulations
Each simulation runs 1000 3D t-test cases (40 datasets, 1 sample) and does cluster-detection (fixed cluster-size threshold, not ETAC – for speed)
Left column: all 40,000 inputs are independent in each simulation
Right column: inputs resampled from 198 datasets in each simulation
Independent
dataset
Resampled
datasets

## Slide 52: ETAC: FPR spatial density
small
max
Fairly uniform in space
20000 simulations
Notes: 20,000 simulations from rsFMRI datasets

## Slide 53: Global Threshold: FPR density
small
max
Not so uniform in space
Notes: Single blur case (8 mm); single p threshold (0.002)

## Slide 54: Task Detection Power: ETAC minus Global Threshold
UCLA Phenomics study (pamenc vs control task)
20 (out of 81) subjects per test
➾ data from OpenFMRI web site
500 simulations
Notes: Main point: ETAC has no LOSS of power, and a little gain – in this one case

## Slide 55: ETAC activation mask (2% FPR, all 81 subjects)
UCLA Phenomics study (pamenc vs control task)
20 (out of 81) subjects per test
➾ data from OpenFMRI web site
Notes: Main point: ETAC has no LOSS of power, and a little gain – in this one case

## Slide 56: Using ETAC
ETAC algorithm: program 3dXClustSim
User adds options to 3dttest++ to run ETAC after the group t-tests are done
  –ETAC to enable the algorithm
  –ETAC_blur to specify blur cases to use
  –ETAC_opt to specify thresholding options
    To change from default per-voxel p-values of 0.0100 0.0056 0.0031 0.0018 0.0010
    To change default clustering parameters NN=2 FOM= 2-sided tests goal=αGoal=5%
Notes: For the AFNI users

## Slide 57: ETAC Sample Command
3dttest++
-setA datasets
-setB datasets { other options here ... }
-prefix Gtest.nii
-prefix_clustsim GtestX
-ETAC
-ETAC_blur 6 12
-ETAC_opt
sid=2:pthr=0.01,0.003,0.001:name=TestA
-ETAC_opt
sid=1:pthr=0.01,0.003,0.001:name=TestB
Combines with any other blurring
Notes: If you use –ETAC_blur, then single subject analysis should be done without blurring

## Slide 58: ETAC Sample Outputs
Gtest.nii
Gtest.B6.0.nii
GtestX.B6.0.5percent.txt
GtestX.TestA.ETAC.mthresh.B6.0.nii
GtestX.TestA.ETACmask.2sid.nii
GtestX.TestB.ETAC.mthresh.B6.0.nii
GtestX.TestB.ETACmask.1pos.nii
GtestX.TestB.ETACmask.1neg.nii
Plus a set of B12.0 outputs
Notes: ETACmask outputs  main result of direct interest
ETAC.mthresh outputs  used if want to apply thresholds yourself

## Slide 59: ETAC Sample Outputs
Gtest.nii
Gtest.B6.0.nii
GtestX.B6.0.5percent.txt
GtestX.TestA.ETAC.mthresh.B6.0.nii
GtestX.TestA.ETACmask.2sid.nii
GtestX.TestB.ETAC.mthresh.B6.0.nii
GtestX.TestB.ETACmask.1pos.nii
GtestX.TestB.ETACmask.1neg.nii
The main t-test output file, unthresholded

## Slide 60: ETAC Sample Outputs
Gtest.nii
Gtest.B6.0.nii
GtestX.B6.0.5percent.txt
GtestX.TestA.ETAC.mthresh.B6.0.nii
GtestX.TestA.ETACmask.2sid.nii
GtestX.TestB.ETAC.mthresh.B6.0.nii
GtestX.TestB.ETACmask.1pos.nii
GtestX.TestB.ETACmask.1neg.nii
t-test output file, with 6 mm extra blurring

## Slide 61: ETAC Sample Outputs
Gtest.nii
Gtest.B6.0.nii
GtestX.B6.0.5percent.txt
GtestX.TestA.ETAC.mthresh.B6.0.nii
GtestX.TestA.ETACmask.2sid.nii
GtestX.TestB.ETAC.mthresh.B6.0.nii
GtestX.TestB.ETACmask.1pos.nii
GtestX.TestB.ETACmask.1neg.nii
Multi-threshold dataset for blur=6 mm, 3 p-values

## Slide 62: ETAC Sample Outputs
Gtest.nii
Gtest.B6.0.nii
GtestX.B6.0.5percent.txt
GtestX.TestA.ETAC.mthresh.B6.0.nii
GtestX.TestA.ETACmask.2sid.nii
GtestX.TestB.ETAC.mthresh.B6.0.nii
GtestX.TestB.ETACmask.1pos.nii
GtestX.TestB.ETACmask.1neg.nii
Multi-thresholded mask for Gtest.nii (2 blurs, 3 p’s)

## Slide 63: ETAC Sample Outputs
GtestX.B6.0.5percent.txt
Voxel-wise threshold for 5% global FPR, unclustered;
Smaller than Bonferroni correction (spatial correlation)
4.292 = 1-sided 5% FPR
4.465 = 2-sided 5% FPR
You get this “free” when running –ETAC
and/or –Clustsim in 3dttest++
Notes: These statistical threshold values will be lower the Bonferroni corrected values due to the smoothing

## Slide 64: ¿Using ClustSim with ETAC?
Also in 3dttest++: option -Clustsim
  Can combine with –ETAC for comparison
ETAC and ClustSim use lots (40000) of randomized t-tests to create “noise-only” data for cluster FPR analysis (slow)
  1-sample test: randomize signs of t-test residuals
  2-sample test: & inter-sample permutations
  Uses multiple CPUs to help with speed
Why both? To compare results.
Notes: -Clustsim and –ETAC together are mainly just for testing (i.e., for RWCox)

## Slide 65: Images of Multi-Thresh Maps
blur=4mm
blur=12mm
log
scale
200
13000
FOM=
p=0.001
p=0.003
p=0.010
p=0.001
p=0.003
p=0.010
1600
Notes: Blur=8mm not shown

## Slide 66: How ETAC Works
More complex than ClustSim
Must keep cluster-FOM tables for each sub-method and for each voxel
  Some voxels don’t get many “hits”
  Clusters are dilated to get brain coverage
    But FOM for cluster is based on original size
How to apply spatially variable cluster-FOM to a given cluster in real data?
  Sort thresholds for all voxels in real cluster
  Use the 80% point (100% = maximum)
Notes: TMI, but this was a lot of work

## Slide 67: ETAC: Things to be Done - 1
Single-subject via mixed-model ACF
  Spatially non-stationary? A little complex.
ETAC algorithm without voxel equity
  Multi-method with global cluster thresholds
Implementation details (short term):
  Different αGoals in same run (e.g., 2% 3% 4% 5%)
  Apply multi-thresholds to other t-volumes in 3dttest++ output
    e.g., 1-sample results in 2-sample tests
  Other cluster-FOMs (e.g., TFCE’s)?
Notes: When will this happen? A good question.

## Slide 68: ETAC: Things to be Done - 2
Test more null cases for FPR
  3dttest++ options, such as covariates
    Do multi-threshold maps from the main effect apply to the extra t-tests, such as covariates and 1-sample results in 2-sample tests?
      And give approximately the desired FPR?
    Or does ETAC need to be run separately for each t-test included in the output? 
  Resting state FMRI seed-based correlation maps (all tests up to now are task-based)
  Other scenarios?
Notes: When will this happen? A good question.

## Slide 69: ETAC: Things to be Done - 3
Test more positive cases for power
  Task-based and resting state
  Need large number of subjects for this work
    So can test subsets of different sizes
    And draw lots of random sub-collections
  For task cases, need a variety of conditions
    So can cover large parts of brain
    Including conditions with small (focal) activations, such as amygdala
      Will ETAC work well for such cases?

## Slide 70: ETAC: Things to be Done - 4
Extend method to work on surface domains, not just 3D volumes
  Will need a lot of work        
  Need to write ClustSim for surfaces
  Need to write ETAC (multi-thresholding and FPR solving) for surfaces
  Or for mixed 2D+3D domains, as in the CIFTI-format data (e.g., HCP)
    Cortical surfaces plus basal ganglia volumes
    ETAC is based on topology not on geometry
Notes: When will this happen? In my next incarnation

## Slide 71: ETAC: Things to be Done - 5
Should ETAC output show you which sub-methods a voxel passed?
  e.g., which p-values, which blur cases?
Need experience with actual users/actual studies to find things out:
  What other outputs would be interesting?
  How useful is ETAC now, compared to other methods for global thresholding?
These 5 slides are just part of the list …
Notes: When will this happen? In my next incarnation

## Slide 72: Other Ruminations
With many subjects in a study, does cluster-FOM thresholding continue to make sense?
  More and more of brain will pass test
    Unless looking at a restricted hypothesis, such as brain regions correlated with some subject behavior/condition
  How to interpret such results?
At what point does voxel-wise only thresholding become ”reasonable”?

## Slide 73: Conclusions (At Long Last! )
If 3dttest++ can do your group analysis, ETAC might be your new friend
  Fewer arbitrary thresholding choices 
  No loss of power 
  Not fully tested yet 
  No publication to cite yet 
If you need 3dLME, 3dMVM, etc., then the mixed model ACF method is decent
  With per-voxel p ≤ 0.002
  Publication you can cite 
Notes: Second point is why a non-stationary ACF model for Clustsim is desirable

## Slide 74: AFNI Clustering Papers
Somewhere over the rainbow – ETAC paper
FMRI Clustering and False Positive Rates. PNAS 114: E3370–E3371, 2017.
  https://arxiv.org/abs/1702.04846
  https://doi.org/10.1073/pnas.1614961114
FMRI Clustering in AFNI: False Positive Rates Redux. Brain Connectivity 7:152-171, 2017.
  https://arxiv.org/abs/1702.04845
  https://doi.org/10.1089/brain.2016.0475

## Slide 75: Where It Started
Clear Creek trail, Grand Canyon

## Slide 76: Finally … Thanks
The list of people I should thank is not quite as large as Skewes’ number★ …
MM Klosek. JS Hyde. JR Binder. EA DeYoe. SM Rao.
EA Stein. A Jesmanowicz. MS Beauchamp. BD Ward.
KM Donahue. PA Bandettini. AS Bloom. T Ross.
M Huerta. ZS Saad. K Ropella. B Knutson. J Bobholz.
G Chen. RM Birn. J Ratke. PSF Bellgowan. J Frost.
K Bove-Bettis. R Doucette. RC Reynolds. PP Christidis.
LR Frank. R Desimone. L Ungerleider. KR Hammett.
DS Cohen. DA Jacobson. EC Wong. J Gonzalez-Castillo. D Glen.
P Kundu (AKA IMoM). E Raab. A Martin. S Gotts. PA Taylor.
And YOU, the suffering audience …
★Currently thought to be about 1.4×10316