FreeSurfer Workshop

Peggy Christidis

National Institute of Mental Health

Thursday, November 18, 2004

# GOAL OF FREESURFER WORKSHOP

- Learn to create surfaces using the FreeSurfer software

(Available at http://surfer/nmr.mgh.harvard.edu/download.html)

- Specifically, start with an anatomical scan off of the scanner, and create a surface by following the steps shown in the flowchart below.

- Transfer surface to SUMA (Z. Saad, 2002) to overlay functional data.

STEPS INVOLVED (FLOWCHART)

1) VOLUME PRE-PROCESSING

Starting with raw data (I-files):

- Create AFNI dataset using to3d.

Usage:  to3d [-options] <image files>

Class Example: cd lc_play

foreach x (1 2 3 4)

to3d -prefix mprage{$x}  00{$x}/I.*

end

- Perform an intensity normalization using the AFNI program 3dUniformize.

Usage: 3dUniformize   -anat <AFNI dataset>   -prefix <prefix name>

Class Example:

foreach x (1 2 3 4)

3dUniformize  -quiet -anat mprage{$x}+orig   -prefix mprage{$x}_n3

end

*Note:  An N3 (Non-parametric Non-uniform intensity Normalization) correction can be done with the Montreal Neurological Institute tool “nu_correct”.  Substantially improves the accuracy of anatomical analysis techniques such as tissue classification and cortical surface extraction.  For more information, see:

- Sled, J. G., A. P. Zijdenbos, et al. (1998). "A nonparametric method for automatic correction of intensity nonuniformity in MRI data." IEEE Trans Med Imaging 17(1): 87-97.)

- Register your datasets using AFNI’s 3dvolreg.

Usage: 3dvolreg -base <bname> -prefix <pname> <target file>

Class Example:

foreach x  (2 3 4)

3dvolreg  -base mprage1_n3+orig    -prefix mprage{$x}_n3vr \

mprage{$x}_n3+orig

end

- Average your datasets using AFNI’s 3dmerge or 3dMean.

Usage: 3dMean -prefix <pname> <datasets …>

Class Example:

3dMean   -prefix  mprage_avg   mprage*_n3vr+orig.BRIK   mprage1_n3+orig

- Create FreeSurfer’s directory structure:

Usage: mksubjdirs <subject name>

Class Example:

mksubjdirs  lc_avg

lc_play/

bem/        label/       morph/       mpg/     mri/      rgb/     scripts/    surf/     tiff/       tmp/

T1/       aparc/    brain/    filled/     orig/     tmp/    transforms/    wm/

- Convert volume into FreeSurfer COR format:

Usage: mri_convert <orig_dataset>  .

Class Example:

cp  mprage_avg+orig.*  lc_avg/mri/orig

cd  lc_avg/mri/orig

mri_convert  mprage_avg+orig.BRIK  .

2) SEGMENTATION

- From Graphical User Interface (GUI): SubjectTools ( Process Volume

Result: Normalizes intensity, strips skull, and segments white matter.

- From Command Line:

Usage: segment_subject <subject_name>

Class Example:

cd ../../..			(i.e., go back up to  lc_play directory)

option 1:  segment_subject  lc_avg

option 2:  recon-all  -stage1  -stage2  -nomotioncor  -subjid lc_avg

Result: Normalizes intensity, strips skull, segments white matter, AND

cuts planes, fills, tessellates, smoothes, inflates.

- This process takes approximately 10-15 minutes for both the hemispheres.

3) INFLATION (for GUI users only)

- Note: If using the command line option, skip this step and proceed to manual editing.

- From GUI: SubjectTools ( Create Surface

Result: Cuts planes, fills, tessellates, smoothes, inflates surface.

- Now is a good time to look at your inflated surface and check for topologic defects.

(SubjectTools ( Edit  Segmentation)

- This process takes approximately 10-15 minutes for both hemispheres.

4) MANUAL EDITING

- This procedure follows the Create Surface step, once the surface has finished inflating.  It is the only manual step of the standard reconstruction process and may require several iterations.

- Note: The FreeSurfer gurus at MGH mention that this (somewhat painful) step is only required if you wish to proceed with inter-subject averaging and morphometric studies.

- There are two main causes of topologic defects:

  - segmentation errors (i.e. a white matter voxel is incorrectly classified as non-white or vice-versa)

  - non-cortical anatomic structures (e.g. fornix, basal ganglia, ventricles)

- The most common anatomically derived defects that require manual editing are:

- Fornix (results in handles in the hemisphere’s surface)

- Lateral Ventricle (results in a hole in the hemisphere’s surface)

- Basal Ganglia (results in a hole in the hemisphere’s surface)

- Optic Nerve (which doesn't result in topological defects, but interferes with inflation)

- Excellent tutorial available on FreeSurfer Website to guide you through manual editing:

http://surfer.nmr.mgh.harvard.edu/docs/index.html

- Smaller topologic defects can be fixed via “Fix Surface Topology.”

5) RE-INFLATION

- The manual editing and inflation steps should be repeated until all the large topologic defects have been corrected.

- From GUI: SubjectTools ( Create Surface

- From Command Line:

option 1:  inflate_subject  lc_avg

option 2:  recon-all -stage2  -subjid lc_avg

- Note:  Do NOT proceed with “Fix Surface Topology” until you have completed manual editing.

6) FIX SURFACE TOPOLOGY

- Once the surface is free of large anatomically derived defects, the automated topology fixer can be used to remove smaller topological defects.

- From GUI:  SubjectTools ( Fix Surface Topology

- From Command Line:

Usage:  fix_subject <subject_name>

Class Example:

option 1:  fix_subject  lc_avg

option 2:  recon-all -stage3  -subjid lc_avg

- This process takes approximately 2 hrs per hemisphere to run to completion.

7) MAKE FINAL SURFACES

- This step starts a fully automated, two-part background process to create the final left and right hemisphere cortical surfaces. The gray/white boundary is called ?h.white and the gray/csf boundary is called ?h.pial.

- The white and pial surfaces are used to estimate the cortical thickness at all locations on the cortical surface. The thickness estimates are stored in a curv file called ?h.thickness.

- From GUI:  SubjectTools ( Make Final Surface

- From Command Line:

Usage:  make_final_surfaces_subject <subject_name>

Class Example:

option 1: make_final_surfaces_subject  lc_avg

option 2: recon-all  -stage4a  -subjid lc_avg

- The two-part processes take a total of approximately 4-6 hrs per hemisphere to run to completion.

8) CUT AND FLATTEN SURFACE

- This process is optional and provides the user with flattened images of the whole brain or select parts (e.g. occipital lobe) of the brain.

Full Surface Cuts:

Five “relaxation” cuts will need to be made – one across the calcarine sulcus, three radial cuts along the medial surface, and one sagitally oriented cut around the temporal lobe.

- Go to main GUI and select SubjectTools ( Make Full Surface Cuts.

- For each cut, select the points that will form that cut (using the LEFT mouse button).

- Press the CUT LINE button on the TK Surfer Interface to connect the points and form a cut line.  Follow this step for each of the five relaxation cuts.

- Make a final cut that encircles the midline region.  Rather than pressing the CUT LINE button, press the CUT CLOSED LINE button.

- Select a point on the surface outside the midline region.

- Press the CUT AREA button.

- Save the patch as ?h.full.patch.3d

Occipital Cuts:

- Go to main GUI and select SubjectTools ( Make Occip Surface Cuts.

- Select points across the calcarine fissure and press CUT LINE on the TK Surfer Interface.

- Select 3 points to define the cutting plane, two on the medial side and one on the lateral side.

- Choose a fourth point to specify which portion of the surface to keep.

- Make the planar cut by pressing the CUT PLANE button on the TK Surfer Interface.

- Save the patch as ?h.occip.patch.3d

Flatten Surface:

- From GUI:  SubjectTools ( Flatten Surface

- From Command Line:

Usage:  mris_flatten <input patch> <output patch>

Class Example:

mris_flatten ?h.full.patch.3d  ?h.full.patch.flat

- This process takes approximately 8-10 hrs per full hemisphere and 6 hours per hemisphere for the occipital surface.

9) VOLUME/SURFACE POST-PROCESSING

- Your surfaces are now ready and can be transferred over to SUMA.

- For more details on how to use SUMA visit:

http://afni.nimh.nih.gov/ssc/ziad/SUMA

# Text boxes

Cut & Flatten Surface

Volume/Surface Post-processing

Make Final Surfaces

Fix Surface Topology

Inflation

Re-inflation

Manual Editing

Segmentation

Volume

Pre-processing

lc_avg/